| Results of Annual Simulation |  |
| --- | --- |
| Collector Surface Area Irradiation: | 10.63 MWh | 1,650.30 kWh/m² |
| Energy Produced by Collectors: | 4.58 MWh | 711.06 kWh/m² |
| Energy Produced by Collector Loop: | 4.24 MWh | 657.79 kWh/m² |
| DHW Heating Energy Supply: | 5.14 MWh |  |
| Solar Contribution to DHW: | 3.99 MWh |  |
| Energy from Auxiliary Heating: | 1.74 MWh |  |

| Natural Gas Savings: | 500.4 m³ |
| --- | --- |
| CO2 Emissions Avoided: | 1135.36 kg |
| DHW Solar Fraction: | 69.7 % |
| System Efficiency: | 37.5 % |

| Project Data |  |
| --- | --- |
| Location: | Portland ME |
| Weather Data Record: | "Portland ME" |
| Global Radiation Annual Total: | 1421.88 kWh |
| Latitude: | 43.65 ° |

| Basic Data |  |
| --- | --- |
| Domestic Hot Water |  |
| Average Daily Consumption: | 378 l |
| Desired Temperature: | 45 °C |
| Load Profile: | Detached House (evening max) |
| Cold Water Temperature: | 12 °C | 14 °C |

| System Components |  |
| --- | --- |
| Collector Loop |  |
| Manufacturer: | Schuco Solar |
| Type: |  | Slim-line V |
| Number: | 3.00 |
| Total Gross Surface Area: | 6.96 m² |
| Total Active Solar Surface Area: | 6.444 m² |
| Inclination (Tilt Angle): | 45 ° |
| Azimuth: | 0 ° |
| DHW Standby Tank |  |
| Manufacturer: | T*SOL Database |
| Type: |  | DHW Tank - 300 |
| Volume | 300 l |
| Solar Preheating Tank (S) |  |
| Manufacturer: | T*SOL Database |
| Type: |  | DHW Tank - 400 |
| Volume | 400 l |
| Auxiliary Heating |  |
| Manufacturer: | T*SOL Database |
| Type: |  | Gas Boiler - 12 |
| Output: | 12 kW |

|  | Original T*SOL Database |  | With Test Report |  | Proof of Conformity Available |
| --- | --- | --- | --- | --- | --- |

These calculations were carried out by T*SOL Pro 4.3 - the Simulation Programme for Solar Thermal Heating Systems. The results are determined by a mathematical model calculation with variable time steps of up to 6 minutes. Actual yields can deviate from these values due to fluctuations in the weather, consumption and other factors.The Schematic System Diagram above does not represent and cannot replace a full technical drawing of the solar system.